## Slide 2: "Unleashing the Power of P300 Spellers: Elevating Performance through Cutting-Edge Feature Extraction Analysis"
BCI Spring Hackathon, April 28, 2024
Diptyajit Das, Bhawna Kapoor, Tanaya Das, Zahra Maleki, and Puneet Tomar
Email: tomarp@pm.me

## Slide 3: Problem Statement Can we design a novel classifier that can improve P300 Speller performance based on features ?
P3/P300?
Prominent positive event-related brain potential (ERP)
SOTA
the row/column
Row/Column speller (RC)
Subjects paid attention to speller flashes with multiple character at once.
Time-variant Linear Discriminant Analysis (TVLDA)
Subjects: 5, EEG data: 8-channel, Sampling Rate : 250 Hz
TVLDA outperformed LDA classifier with a high accuracy (~90%)
[1] Ref. https://doi.org/10.1016/j.neulet.2009.06.045

## Slide 4: P300 speller
What is P3/P300?
Prominent positive event-related potential (ERP) in EEG.
Reflects brain activity approx. 300 ms after the target stimuli.
Popular in BCI paradigm: easy to detect, high accuracy and speed.
[2] Ref. https://doi.org/10.1016/j.clinph.2023.11.014.

## Slide 5: Pre-Processing EEG
Steps performed:
MNE styled Raw object creation (raw data)
EEG montage/common average
Bandpass filtering ( 1-30 Hz )
Epochs creation (-0.1 to 0.8s)
Plot evoked for quality control
Start

## Slide 6: Evoked EEG plots
Plot 1: Evoked signal from one subject (target)
Plot 3: Trigger information
Plot 2: Evoked signal from one subject (non-target)

## Slide 7: Pipeline Workflow
Extracted Power Spectrum Density (PSDs) features
Normalization of features
Oversampling to address class imbalance
Defining a RFClassifier
Training of classifier
Evaluation of model
Start
End

## Slide 8: RESULTS (1)
Plot 5: Accuracy of RF classifier for each subject
All subjects achieved more than 98% accuracy using RF classifier

## Slide 9: RESULTS (2)
Plot 6 : Metrics obtained for RF classifier

## Slide 10: RESULTS (3)
Plot 7: Confusion matrix obtained for each subject

## Slide 11: Conclusion Future Work
Achieved the best possible performance (ACC > 98%) using RF classifier
Performance of RF > Logistic regression > TVLDA
Different combination of TD & FD features can be evaluated
Model can be trained on collective vs individual samples

## Slide 12: Code is available at github
Diptyajit Das, Bhawna Kapoor, Tanaya Das, Zahra Maleki, and Puneet Tomar
Email: tomarp@pm.me

## Slide 13: We are Neuroide !!